## Slide 1
Non-Uniform Quantization as Shift-Decodable Normalized Bins
Core Idea
floating plane
→
normalized plane
→
non-uniform bin plane
→
shift plane

## Slide 2
Quantization as Plane Mapping
Weights begin in floating space:
( w \in \mathbb{R} )
Normalize magnitude:
( u = \frac{|w|}{\alpha_g} \quad \Rightarrow \quad u \in [0,1] )
Then quantization chooses a bin:
( u \rightarrow m_q )
Final signed weight:
( w_q = s \cdot \alpha_g \cdot m_q )
Shift-Decodable Quantization
2

## Slide 3
Uniform Quantization View
Uniform quantization divides into equal bins. For 3-bit magnitude:
Uniform quantization divides ( [0,1] ) into equal bins. For 3-bit magnitude:
The code is interpreted as an integer:
( \mathcal{M}_{uniform} = \left\{ 0, \frac{1}{7}, \frac{2}{7}, \ldots, 1 \right\} )
The code is interpreted as an integer: ( 101_2 = 5 \quad \Rightarrow \quad m_q = \frac{5}{7} )
So uniform quantization is:
code integer uniform bin
code ( \rightarrow ) integer ( \rightarrow ) uniform bin
Shift-Decodable Quantization
3

## Slide 4
Proposed Non-Uniform Bin Plane
Instead of equal bins, use non-uniform bins in the normalized plane:
( \mathcal{M} = \{0,\ 0.0625,\ 0.125,\ 0.1875,\ 0.25,\ 0.375,\ 0.5,\ 0.625\} )
Equivalent shift form:
( \mathcal{M} = \{0,\ 2^{-4},\ 2^{-3},\ 2^{-3}+2^{-4},\ 2^{-2},\ 2^{-2}+2^{-3},\ 2^{-1},\ 2^{-1}+2^{-3}\} )
This places more bins near zero, where weight density is usually higher. Non-uniform quantization is motivated by the fact that neural-network weights are concentrated near zero, while power-of-two forms can replace multiplication with shifting.
Key insight: More precision where weights are dense + shift operations replace multipliers.
Shift-Decodable Quantization
4

## Slide 5
Important Difference
The code is not interpreted as a normal integer.
Uniform
( 101_2 = 5 )
( m_q = \frac{5}{7} )
Proposed
( 101 \rightarrow 2^{-2} + 2^{-3} )
( m_q = 0.25 + 0.125 = 0.375 )
So the code means:
shift pattern, not integer value
Shift-Decodable Quantization
5

## Slide 6
Sign + Magnitude Storage
For symmetric LLM weight quantization:
( \text{stored code} = [\text{sign bit},\ \text{magnitude bits}] )
Magnitude:
( m_q \in \mathcal{M} )
Sign:
( s \in \{-1, +1\} )
Final weight:
( w_q = s \cdot \alpha_g \cdot m_q )
For 3-bit magnitude plus sign: bits per weight.
For 3-bit magnitude plus sign: ( B_{total} = 4 ) bits per weight.
Shift-Decodable Quantization
6

## Slide 7
Why Dequantization Becomes Fast
Example:
Example: ( m_q = 2^{-2} + 2^{-3} )
Then:
( w_q x = s \cdot \alpha_g \cdot (2^{-2}x + 2^{-3}x) )
Hardware:
( 2^{-2}x = x \gg 2 )
( 2^{-3}x = x \gg 3 )
So:
( w_q x = s \cdot \alpha_g \cdot [(x \gg 2) + (x \gg 3)] )
No arbitrary coefficient multiplication is needed inside the inner loop.
Shift-Decodable Quantization
7

## Slide 8
Decoder Instead of Value LUT
A value LUT would do:
then:
( 101 \rightarrow 0.375 )
then: ( 0.375 \times x )
Our method does:
then:
( 101 \rightarrow E_2 = 1,\ E_3 = 1 )
then: ( (x \gg 2) + (x \gg 3) )
So the code produces shift-enable signals, not a stored floating-point value. The decoder generates control signals for the datapath, bypassing the need for a coefficient lookup and multiply operation.
Shift-Decodable Quantization
8

## Slide 9
3-Bit Boolean Decoder
Let magnitude code be:
Let magnitude code be: ( c = c_2 c_1 c_0 )
Define shift-enable wires:
:
:
:
:
( E_1 ): ( x \gg 1 )
( E_2 ): ( x \gg 2 )
( E_3 ): ( x \gg 3 )
( E_4 ): ( x \gg 4 )
Boolean equations:
( E_1 = c_2 \land c_1 )
( E_2 = c_2 \land \neg c_1 )
( E_3 = (\neg c_2 \land c_1) \lor (c_2 \land c_0) )
( E_4 = \neg c_2 \land c_0 )
Shift-Decodable Quantization
9

## Slide 10
Decoder Truth Table
Code | E₁ | E₂ | E₃ | E₄ | Value
000 | 0 | 0 | 0 | 0 | 0
001 | 0 | 0 | 0 | 1 | \(2^{-4}\)
010 | 0 | 0 | 1 | 0 | \(2^{-3}\)
011 | 0 | 0 | 1 | 1 | \(2^{-3} + 2^{-4}\)
100 | 0 | 1 | 0 | 0 | \(2^{-2}\)
101 | 0 | 1 | 1 | 0 | \(2^{-2} + 2^{-3}\)
110 | 1 | 0 | 0 | 0 | \(2^{-1}\)
111 | 1 | 0 | 1 | 0 | \(2^{-1} + 2^{-3}\)
Shift-Decodable Quantization
10

## Slide 11
Hardware Datapath
( [c_2, c_1, c_0] \rightarrow [E_1, E_2, E_3, E_4] )
Compute shifted partial sums:
( z = E_1(x \gg 1) + E_2(x \gg 2) + E_3(x \gg 3) + E_4(x \gg 4) )
Apply sign:
( z_s = \begin{cases} z, & s = +1 \\ -z, & s = -1 \end{cases} )
Apply group scale:
( y = \alpha_g \cdot z_s )
The entire datapath consists of decoder logic shift-add tree sign mux final scale.
The entire datapath consists of decoder logic ( \rightarrow ) shift-add tree ( \rightarrow ) sign mux ( \rightarrow ) final scale.
Shift-Decodable Quantization
11

## Slide 12
Example Walkthrough
Code:
Code: ( 101 )
So:
So: ( c_2 = 1,\quad c_1 = 0,\quad c_0 = 1 )
Decoder output:
( E_2 = 1,\quad E_3 = 1 )
Therefore:
( m_q = 2^{-2} + 2^{-3} )
For activation :
For activation ( x = 16 ):
( z = (16 \gg 2) + (16 \gg 3) )
( z = 4 + 2 = 6 )
Then:
( y = \alpha_g \cdot s \cdot 6 )
Shift-Decodable Quantization
12

## Slide 13
Why Boolean Decoder Can Be Better Than LUT
A value LUT requires:
( \text{code} \rightarrow \text{memory/table read} )
( \rightarrow \text{coefficient} \rightarrow \text{multiply} )
Boolean decoder requires:
( \text{code} \rightarrow \text{AND/OR/NOT gates} )
( \rightarrow \text{shift enables} \rightarrow \text{shift-add} )
FPGA LUTs are commonly described as small truth-table memories for implementing logic functions; in ASIC/custom hardware, the same Boolean equations can be synthesized directly into gates instead of read as stored values.
The decoder eliminates the memory read latency and replaces multiplication with simple shifts and additions.
Shift-Decodable Quantization
13

## Slide 14
LUT vs Boolean Decoder
Design | Decode mechanism | Inner operation
Value LUT | Fetch stored coefficient | Multiply
Shift-pattern LUT | Fetch enable vector | Shift-add
Boolean decoder | Gates generate enable vector | Shift-add
Best custom-hardware path:
Boolean decoder + shift-add datapath
Shift-Decodable Quantization
14

## Slide 15
Delayed Scaling
Instead of applying scale for every individual weight:
( w_q = \alpha_g \cdot s \cdot m_q )
First compute shift-add accumulation:
( A_g = \sum_e 2^{-e} \left[ XM^+_{g,e} - XM^-_{g,e} \right] )
Then apply scale once:
( Y_g = \alpha_g \cdot A_g )
This reduces repeated dequantization overhead — scale is applied once per group, not per weight.
Shift-Decodable Quantization
15

## Slide 16
Matrix-Level Form
Represent a weight group as:
( W_g = \alpha_g \sum_{e \in \mathcal{E}} 2^{-e} \left( M^+_{g,e} - M^-_{g,e} \right) )
Then:
( Y_g = XW_g = \alpha_g \sum_{e \in \mathcal{E}} 2^{-e} \left[ XM^+_{g,e} - XM^-_{g,e} \right] )
This exposes the hardware execution path directly in the matrix multiplication formula.
Shift-Decodable Quantization
16

## Slide 17
Key Claim
The method does not use the low-bit code as an integer.
It uses the code as a compact control word:
code bits Boolean shift decoder shift-add dequantization
code bits ( \rightarrow ) Boolean shift decoder ( \rightarrow ) shift-add dequantization
This gives:
Non-uniform bins
+
Compact storage
+
Fast hardware execution
Shift-Decodable Quantization
17

## Slide 18
Important Caveat
This is not automatically faster on every GPU.
The strongest benefit appears in:
Custom accelerator
ASIC-style PE
Native shift-add datapath
On FPGA, Boolean logic may still map into FPGA LUT primitives, so the advantage over a tiny shift-pattern LUT may be smaller.
The stronger claim is against value-LUT dequantization, where a stored coefficient is fetched and then multiplied.
Shift-Decodable Quantization
18

## Slide 19
Final Summary
Uniform quantization:
( \text{code} \rightarrow \text{integer bin} )
Proposed method:
( \text{code} \rightarrow \text{non-uniform shift bin} )
Fast dequantization:
( m_q x = \sum_{e \in \mathcal{E}(q)} (x \gg e) )
Final weight:
( w_q x = s \cdot \alpha_g \sum_{e \in \mathcal{E}(q)} (x \gg e) )
Final takeaway:
Non-uniform quantization can be hardware-fast
when bins are Boolean-decodable into shifts.