## Slide 1
INTERNAL | HARDWARE R&D
Power-of-Two Quantization
A Unified Hardware Path for Mixed-Precision Inference
Smaller silicon. Lower power. One decoder for every precision.

## Slide 2
Today's Bottleneck: LUT-Based Quantization
Non-uniform quantization stores every level in a table and feeds a multiplier per weight
SRAM LUT
idx 0 → -1.421
idx 1 → -0.731
idx 2 → -0.296
idx 3 → -0.085
idx 4 → 0.085
... → ...
idx 15 → 1.421
×
multiplier
Stored, not computed
Every quantization level lives in SRAM — area scales with bit-width
Read latency + power
Address decode + SRAM access on every weight operation
Multiplier still required
After the lookup, a full multiplier is still in the critical path

## Slide 3
Power-of-Two: Multiplication Becomes Shifting
Quantization levels expressed as sums of powers of 2 — no table, no multiplier
THE INSIGHT
z = 10 = 8 + 2 = 23 + 21 ⇒ x · 10 = (x << 3) + (x << 1)
✓
No LUT
Zero stored quantization levels. No SRAM access per weight.
✓
No Multiplier
Replaced by hardwired shifts and a small adder.
✓
Same Codebook,
All Precisions
8-bin, 4-bin, 2-bin share one set of power-of-2 atoms.

## Slide 4
Power-of-Two Hardware: Shift-and-Add
One input fans out to hardwired shifts; enables (E) gate each lane; outputs sum in a single adder
Activation x
e₀
× 1
x << 0
e₁
× 2
x << 1
e₂
× 4
x << 2
e₃
× 8
x << 3
+ Adder
x · z
Amber circles are exponent enables — when off, the lane contributes 0
≤ 2
active lanes at any time
1
addition on the critical path
0
general multipliers needed

## Slide 5
C → E Mapping: The Decoder
Converts stored control bits (C) into the exponent enables (E) that drive the shift-add hardware
C (control bits)
g₁
g₀
r
DECODER
3 AND gates
+ 1 inverter
≈ 1 gate delay
E (exponent enables)
e₃ → × 8
e₂ → × 4
e₁ → × 2
e₀ → × 1
Footprint: roughly the area of a single full-adder cell — and it feeds the shift-add hardware directly.

## Slide 6
One Mapper, Every Precision Mode
The same decoder and shift-add hardware handles 8-bin, 4-bin, and 2-bin weights — no replication
8-bin
3-bit weights
high-saliency channels
4-bin
2-bit weights
medium channels
2-bin
1-bit weights
low-saliency channels
SAME PHYSICAL HARDWARE
C → E Decoder + Shift-and-Add Multiplier + Sign Accumulator
No datapath replication across precisions
Lower precisions clock-gate idle paths for free

## Slide 7
End-to-End Datapath
Stored weights decode once into E enables; activations enter the shift-add hardware as a second input
Stored Weight Bits
C → E Decoder
3 ANDs + 1 INV
Activation x
streams in each cycle
SHIFT + ADD HARDWARE
gated shifts → single adder
E enables (e₀..e₃)
x (activation)
Output: x · w

## Slide 8
BOTTOM LINE
What This Buys Us
Smaller Silicon
Eliminates the LUT SRAM and replaces multipliers with shifters
Lower Power
No SRAM access per weight; idle paths clock-gated in low-precision modes
Faster Critical Path
1-gate decoder + a single adder; no multiplier latency
Mixed-Precision Ready
One unified mapper serves 8-bin, 4-bin, and 2-bin weights